## Slide 1: Experimentální metody při studiu iont – molekulových reakcí a iont – elektronové rekombinace

## Slide 2: Time dependence of the value of recombination rate coefficient for H3+ ions with electrons
Not a simple problem

## Slide 3: Different experiments
Ion Storage Ring
Afterglow plasma
+ No buffer gas
+ Excellent energy resolution
Complicated estimation of cross section from measured data
Rotational temperature of ions in the ring can be >= 300 K
+ Many collisions of ions with buffer gas particles – effective thermalization
+ The measured quantity is thermal rate coefficient
Complicated chemical kinetics
Presence of third bodies can influence the recombination

## Slide 4: Ion storage ring
Figure 1: Design model of the CSR showing the electrostatic ion optical elements (enlarged in circuits), the injection line, the electron cooler (straight section at the right side) and the reaction microscope (straight section at the left side)
(A) Scheme of the CSR ring structure with the injected and stored HeH+ ion beam (red), merged electron beam (blue), reaction products (green), and particle detector. (B) Reaction scheme and position-sensitive detection of coincident fragments. (C) Equilibrium rotational state populations of HeH+ for previous studies (300 K) and the estimated radiation field in the CSR.

## Slide 5: Rekombinace iontů ve specifickém kvantovém stavu

## Slide 6: Rekombination of H3+ ions with electrons
Neutral assisted ternary recombination:
Electron assisted ternary recombination:
Formation of H5+ and its subsequent recombination with electrons:
Glosík J., Dohnal P. et al., Plasma Sources Sci. Technol. 24(6), 065017, 2015

## Slide 7: Aparatura SA-CRDS
CRDS – Cavity Ring Down Spectroscopy
SA – Stationary Afterglow
Vysoce odrazivé zrcadlo
  Průměr výbojové trubice – 1.5 cm
  He buffer gas flow ~ 400 – 1600 sccm
  Tlak ~ 200 – 1500 Pa
  Teplotní rozsah ~ 77 – 300 K

## Slide 8: Cavity ringdown spectroscopy
Původní použití pro měření odrazivosti zrcadel (viz Herbelin et al. 1980).
Později pozorováno, že ring-down time závisí na absorpci mezi zrcadly (viz O‘Keefe et al. 1988)
Herbelin et al., Appl. Opt. 19, 144, 1980.
O‘Keefe et al., Rev. Sci. Instrum. 59, 2544, 1988.
Vysoce odrazivá zrcadla firmy Layertec (průměr 6.3 mm, odrazivost R = 99.99 %)

## Slide 9: SA-CRDS
Měří se časový vývoj koncentrace iontů (jednotlivých kvantových stavů)
Kinetická teplota iontů určena z Dopplerova rozšíření absorpčíních čar
Rotační teplota určena z relativní populace jednotlivých stavů

## Slide 10: Cryo-SA-CRDS

## Slide 11: Cryo-SA-CRDS

## Slide 12: Cryo-SA-CRDS
Plašil, R; Dohnal, P; Kálosi, Á; Roučka, Š; Shapko, D; Rednyk, S; Johnsen, R; Glosík, J, Rev. Sci. Instrum., 89: 063116, 2018.

## Slide 13: H3+ (again)
The lowest rotational states of the vibrational ground state
Para
Ortho
I = 1/2
I = 3/2

## Slide 14: Cryo-SA-CRDS
At 30 K, we can change the population of the of the lowest state of H3+ from 40% to 80% of all ions. The rest of the ions are mainly in the (1,0) state.

## Slide 15: Rekombinace iontů H3+ ve specifickém kvantovém stavu

## Slide 16
Kombinace CRDS a mikrovlnné diagnostiky

## Slide 17: Studovaný iont není v plazmatu dominantní

## Slide 18: Proudící dohasínající plazma

## Slide 19: Proudící dohasínající plazma

## Slide 20: FALP, SIFT, SIFDT
FALP – Flowing Afterglow with Langmuir Probe
SIFT – Selective Ion Flow Tube
SIFDT – Selective Ion Flow Drift Tube

## Slide 21: FALP, SIFT, SIFDT
FALP – studium elektron – iontové rekombinace
SIFT – studium reakcí iontů s molekulami
Měření pohyblivosti iontů

## Slide 22: Cryo-FALP II
  Cryogenic Flowing Afterglow with Langmuir Probe
  Průměr proudové trubice – 5 cm
  He buffer gas flow ~ 2500– 6000 sccm
  Tlak ~ 200 – 2000 Pa
  Teplotní rozsah ~ 40 – 300 K

## Slide 23: Cryo-FALP II
Měří se vývoj koncentrace elektronů podél proudové trubice (tedy v čase)
Je možno měřit energetickou distribuční funkci elektronů a jejich teplotu

## Slide 24: Rekombinace Ar+ s elektrony, závislost na ne
Kotrík T., Dohnal P., Roučka Š., Jusko P., Plašil R., Glosík J., Johnsen R., Phys. Rev. A 83, 032720, 2011.
Kotrík T., Dohnal P., Rubovič P., Plašil R., Roučka Š., Opanasiuk S., Glosík J., Eur. Phys. J.-Appl. Phys. 56, 24011, 2011.

## Slide 25: Rekombinace Ar+ s elektrony, závislost na tlaku He
Dohnal P., Rubovič P., Kotrík T., Hejduk M., Plašil R., Johnsen R., Glosík J., Phys. Rev. A 87, 052716, 2013.

## Slide 26: Kalibrace Langmuirovy sondy
Rekombinace O2+ je dobře známa (velké množství studií v posledních 50 letech)
Tříčásticová rekombinace (heliem asistovaná) je při daných podmínkách zanedbatelná
Cílem je co nejpřesnější určení absolutní hodnoty koncentrace elektronů

## Slide 27: 22 rf pole ion trap
Many configurations for different experiments
Cold Heads at 22PT and H atom source work down to 11 K a 7 K
Ions produced in Storage Ion Source (SIS)
Only ions selected by QP mass filter enter the trap
After set storage time, the ions from the trap are mass selected and detected by MCP

## Slide 28: 22 rf pole ion trap

## Slide 29: O- + D2
Plašil, R; Tran, TD; Roučka, Š; Jusko, P; Mulin, D; Zymak, I; Rednyk, S; Kovalenko, A; Dohnal, P; Glosík, J; Houfek, K; Táborský, J; Cížek, M, Phys. Rev. A, 96 (6): 062703 ,2017.

## Slide 30: C2+ + H2