## Slide 1: Experimental methods for studies of ion – molecule reactions and of ion – electron recombination

## Slide 2: Time dependence of the value of recombination rate coefficient for H3+ ions with electrons
Not a simple problem

## Slide 3: Different experiments
Ion Storage Ring
Afterglow plasma
+ No buffer gas
+ Excellent energy resolution
Complicated estimation of cross section from measured data
Rotational temperature of ions in the ring can be >= 300 K
+ Many collisions of ions with buffer gas particles – effective thermalization
+ The measured quantity is thermal rate coefficient
Complicated chemical kinetics
Presence of third bodies can influence the recombination

## Slide 4: Ion storage ring
Figure 1: Design model of the CSR showing the electrostatic ion optical elements (enlarged in circuits), the injection line, the electron cooler (straight section at the right side) and the reaction microscope (straight section at the left side)
(A) Scheme of the CSR ring structure with the injected and stored HeH+ ion beam (red), merged electron beam (blue), reaction products (green), and particle detector. (B) Reaction scheme and position-sensitive detection of coincident fragments. (C) Equilibrium rotational state populations of HeH+ for previous studies (300 K) and the estimated radiation field in the CSR.

## Slide 5: Recombination of ions in specific quantum state

## Slide 6: Rekombination of H3+ ions with electrons
Neutral assisted ternary recombination:
Electron assisted ternary recombination:
Formation of H5+ and its subsequent recombination with electrons:
Glosík J., Dohnal P. et al., Plasma Sources Sci. Technol. 24(6), 065017, 2015

## Slide 7: Stationary afterglow plasma
Combination of Stationary afterglow and absorption spectroscopy

## Slide 8: Stationary afterglow plasma
AISA – Advanced Integrated Stationary Afterglow
Mass spectrometer + Langmuir probe diagnostics
Phys. Rev. Lett., 88 (4): Art. No. 044802 (4 pages), 2002.

## Slide 9: Stationary afterglow plasma
Microwave diagnostics + mass spectrometry

## Slide 10
Microwave diagnostics of plasma
Plasma conductivity
Change of resonant frequency and resonator quality:
Plasma frequency

## Slide 11: Microwave diagnostics of plasma
Sicha et al., Czech. J. Phys. B 20, 684, 1970
From the shift of resonant frequency we can get electron number density

## Slide 12: Microwave diagnostics of plasma
Electron number density measurement

## Slide 13: SA-CRDS apparatus
CRDS – Cavity Ring Down Spectroscopy
SA – Stationary Afterglow
Highly reflective mirror
  Discharge tube diameter– 1.5 cm
  He buffer gas flow ~ 400 – 1600 sccm
  Pressure ~ 200 – 1500 Pa
  Temperature range ~ 77 – 300 K

## Slide 14: Cavity ringdown spectroscopy
First used for mirror reflectivity determination (Herbelin et al. 1980).
Later, the dependence of ring-down time on absorption between the mirrors was observed (O‘Keefe et al. 1988)
Herbelin et al., Appl. Opt. 19, 144, 1980.
O‘Keefe et al., Rev. Sci. Instrum. 59, 2544, 1988.
Highly reflective mirrors by Layertec (diameter 6.3 mm, reflectivity R = 99.99 %)

## Slide 15: SA-CRDS
The time evolution of ion number density is measured (of particular quantum states)
Kinetic temperature can be determined from Doppler broadening of absorption lines
Rotational temperature is given by relative populations of rotational states

## Slide 16: Cryo-SA-CRDS

## Slide 17: Cryo-SA-CRDS

## Slide 18: Cryo-SA-CRDS
Plašil, R; Dohnal, P; Kálosi, Á; Roučka, Š; Shapko, D; Rednyk, S; Johnsen, R; Glosík, J, Rev. Sci. Instrum., 89: 063116, 2018.

## Slide 19: H3+ (again)
The lowest rotational states of the vibrational ground state
Para
Ortho
I = 1/2
I = 3/2

## Slide 20: Cryo-SA-CRDS
At 30 K, we can change the population of the of the lowest state of H3+ from 40% to 80% of all ions. The rest of the ions are mainly in the (1,0) state.

## Slide 21: Rekombination of H3+ ions in specific quantum state

## Slide 22
Combination of CRDS and microwave diagnostics

## Slide 23: Studied ion is not dominant in plasma

## Slide 24: Flowing afterglow plasma

## Slide 25: Flowing afterglow plasma

## Slide 26: FALP, SIFT, SIFDT
FALP – Flowing Afterglow with Langmuir Probe
SIFT – Selective Ion Flow Tube
SIFDT – Selective Ion Flow Drift Tube

## Slide 27: FALP, SIFT, SIFDT
FALP – study of electron – ion recombination
SIFT – study of ion – molecule reactions
Measurement of ion mobility

## Slide 28: Cryo-FALP II
  Cryogenic Flowing Afterglow with Langmuir Probe
  Flowtube diameter – 5 cm
  He buffer gas flow ~ 2500– 6000 sccm
  Pressure ~ 200 – 2000 Pa
  Temperature range ~ 40 – 300 K

## Slide 29: Cryo-FALP II
The evolution of electron number density along the flowtube (i.e. in time) is measured
It is possible to determine the electron energy distribution function and their temperature

## Slide 30: Recombination of Ar+ ions with electrons, dependence on ne
Kotrík T., Dohnal P., Roučka Š., Jusko P., Plašil R., Glosík J., Johnsen R., Phys. Rev. A 83, 032720, 2011.
Kotrík T., Dohnal P., Rubovič P., Plašil R., Roučka Š., Opanasiuk S., Glosík J., Eur. Phys. J.-Appl. Phys. 56, 24011, 2011.

## Slide 31: Recombination of Ar+ ions with electrons, dependence on helium pressure
Dohnal P., Rubovič P., Kotrík T., Hejduk M., Plašil R., Johnsen R., Glosík J., Phys. Rev. A 87, 052716, 2013.

## Slide 32: Calibration of Langmuir Probe
Rekombination of O2+ ions with electrons is a well known process (many studies in last 50 years)
Three body (helium assisted) recombination is at given conditions negligible
The goal is to determine the electron number density with the best possible precision

## Slide 33: 22 rf pole ion trap
Many configurations for different experiments
Cold Heads at 22PT and H atom source work down to 11 K a 7 K
Ions produced in Storage Ion Source (SIS)
Only ions selected by QP mass filter enter the trap
After set storage time, the ions from the trap are mass selected and detected by MCP

## Slide 34: 22 rf pole ion trap

## Slide 35: O- + D2
Plašil, R; Tran, TD; Roučka, Š; Jusko, P; Mulin, D; Zymak, I; Rednyk, S; Kovalenko, A; Dohnal, P; Glosík, J; Houfek, K; Táborský, J; Cížek, M, Phys. Rev. A, 96 (6): 062703 ,2017.

## Slide 36: C2+ + H2