## Slide 1: Electroencephalography, consciousness, sleep, circadian rhythm
Jan Kudláček
2024-04-17
kudlaceksystem@gmail.com

## Slide 2: Electroencephalography (EEG)
Alpha activity
Hans Berger
(1873-1941)
Electroencephalograph
(1928)
Electroencephalogram
(1928)
1 s

## Slide 3: Scalp EEG
Notes: Nase práce vychází z klinických pozorování

## Slide 4: Electroencephalography(EEG)
Recording of electrical potentials caused by the brain activity
  Electroencephalograph – instrument
  Electroencephalogram – recording
Method of functional examination
  Epilepsy
  Sleep disorders
  Research
Weak signal
  In the order of 100 µV (compared to e.g. ECG which is around 1 mV)
  Frequency 1 – 100 Hz (typically sampled at 256 Hz or 1 kHz)
  Electrode impedance several kOhm
  One electrode records approx. 2.5 x 2.5 cm

## Slide 5
Cellular mechanisms of the EEG
Pyramidal
neuron
Apical dendritic tree
Soma
Main source of EEG
  Synaptic activity on pyramidal neurons
Pyramidal neurons
  Main projection neurons in the cortex
  Apical dendrites perpendicular to the brain surface
Extracellular currents and electric fields
  Synaptic activity
  Almost no contribution of action potentials
Two pyramidal neurons

## Slide 6: Resting membrane potential
0 mV
-65 mV

## Slide 7: Excitatory synapse
Glutamate
Na+
Na+
Ca2+
Ca2+
Postsynaptic membrane
Presynaptic terminal
AMPA and NMDA receptors
Excitatory postsynaptic potential
(EPSP)
Ca2+
Ca2+
Na+
Ca2+
Na+
Na+
Glutamate

## Slide 8: Inhibitory synapse
Glutamate
Postsynaptic membrane
Presynaptic terminal
AMPA and NMDA receptors
Glutamate
Ca2+
GABA
Interneuron
GABA-A receptors
Cl-
Cl-
Cl-
Cl-
Ca2+
Inhibitory postsynaptic potential
(IPSP)

## Slide 9: Patch clamp
Recording from a single cell
Brain slices
Cell cultures
In vivo
Whole-cell patch clamp

## Slide 10: Spontaneous postsynaptic currents

## Slide 11: Depolarizing pulses, action potentials
Pyramidal neuron
Parvalbumine-positive inhibitory interneuron

## Slide 12: Origin of EEG signal

## Slide 13: Origin of EEG signal

## Slide 14: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 15: Origin of EEG signal
Extracellular recording
Intracellular recording
Scalp EEG
Extracellular recording

## Slide 16: Origin of EEG signal
Extracellular recording
Intracellular recording
Scalp EEG
Extracellular recording

## Slide 17: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 18: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 19: Origin of EEG signal
Extracellular recording
Intracellular recording
Scalp EEG
Extracellular recording

## Slide 20: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 21: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 22: Origin of EEG signal
Intracellular recording
Extracellular recording
Scalp EEG
Extracellular recording

## Slide 23: Origin of EEG signal
Extracellular recording
Intracellular recording
Scalp EEG
Extracellular recording

## Slide 24: Lines of electric force and equipotential lines
Lines of electric force
(current flow)
+
+
+
+
+
+
+
+
+
+

## Slide 25: Lines of electric force and equipotential lines
Lines of electric force
(current flow)
Equipotential lines
+
+
+
+
+
+
+
+
+
+

## Slide 26: Electric field around a neuron
-100 µV
-300 µV
-400 µV
-500 µV
-200 µV
-600 µV
+100 µV
+300 µV
+400 µV
+500 µV
+200 µV
+600 µV
0 µV
0 µV
EEG
-600 µV
EEG
-300 µV
EEG
+600 µV
EEG
+300 µV

## Slide 27: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 28: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 29: Vzdálenost elektrody od generátoru proudu
-100 µV
-300 µV
-400 µV
-500 µV
-200 µV
-600 µV
+100 µV
+300 µV
+400 µV
+500 µV
+200 µV
+600 µV
0 µV

## Slide 30: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 31: Synchronization of postsynaptic potentials
0.4 s
100 µV
0.4 s
100 µV
Synaptic activity of 100 neurons
Synaptic activity of 100 neurons
Asynchronous (random) activity
Synchronous activity
EEG
EEG

## Slide 32: Synchronization of postsynaptic potentials
0.4 s
100 µV
0.4 s
100 µV
Synaptic activity of 100 neurons
Synchronous synaptic activity
Synchronous synaptic activity
EEG
EEG
Epileptic neuron
(intracellular)

## Slide 33: Synaptic activity and action potentials
0.4 s
100 µV
Asynchronous (random) EPSPs
Asynchronous action potentials
EEG
EEG
0.4 s
100 µV
Synaptic activity of 100 neurons
Synaptic activity of 100 neurons

## Slide 34: Synchronization of action potentials
499 Hz
hippocampus
5 ms
EEG
400 Hz
EEG
EEG
High-frequency oscillation (HFO)

## Slide 35: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 36: Effect of the neuron orientation

## Slide 37: Effect of the neuron orientation

## Slide 38: Magnetoencephalografy

## Slide 39: Morphology, amplitude a duration of EEG waves
Distance from the current generator
Duration of the postsynaptic potentials
Number of synchronous postsynaptic potentials
Position of the electrode with respect to the current generator
Anatomical orientation of the cells generating the currents

## Slide 40: Vliv anatomického uspořádání
EEG

## Slide 41: Vliv anatomického uspořádání
EEG

## Slide 42
Scalp EEG
Intracranial EEG
Local field potentials (LFP)
Extracellularly recorded action potentials
> 1 cm
< 1 cm
~ 1 mm
~ 10 um
Electrodes
Notes: Nase práce vychází z klinických pozorování

## Slide 43: Scalp EEG
Notes: Nase práce vychází z klinických pozorování

## Slide 44
Fp1
Fz
F3
F7
T3
C3
Cz
Pz
P3
T5
Fp2
F4
C4
Scalp EEG – electrode positions
International 10-20 system

## Slide 45
Scalp EEG – electrode positions

## Slide 46: Montage
Positions of electrodes and type of referencing of the signals
Referential montage
  Scalp (active) electrode with respect to a reference (neutral) electorde
Bipolar (sequential) montage
  Scalp (active) electrode with respect to another scalp electorde

## Slide 47
EEG – referential montage

## Slide 48
EEG – referential montage
+
-
1
0
0
0
0
0
0
0
0
0
Reference electrode
1
0
0
0
0
Active electrode
EEG trace
Differential amplifier

## Slide 49
+
-
0
0
0
0
0
-1
0
0
0
0
-1
0
0
0
0
Reference electrode
Active electrode
EEG trace
Differential amplifier
EEG – referential montage

## Slide 50
EEG – longitudinal bipolar montage

## Slide 51
EEG – transversal bipolar montage

## Slide 52
+
-
1
0
0
0
0
0.75
0
0
0
0
Active electrode 1
EEG trace
Differential amplifier
0.25
0
0
0
0
EEG – bipolar montage
Active electrode 2

## Slide 53
+
-
1
0
0
0
0
0
0
0
0
0
1
0
0
0
0
Active electrode 1
EEG trace
Differential amplifier
EEG – bipolar montage
Active electrode 2

## Slide 54
+
-
1 mV
0
0
0
0
-1 mV
0
0
0
0
2 mV
0
0
0
0
Active electrode 1
EEG trace
Differential amplifier
EEG – bipolar montage
Active electrode 2

## Slide 55: Waking EEG

## Slide 56: Temporal lobe epilepsy

## Slide 57: Temporal lobe epilepsy

## Slide 58: Deep structures
Deep structures
  Hippocampus
  Thalamus
  Brain stem
No contribution to scalp EEG
Indirect effect on the EEG

## Slide 59
Supplementary anterior temporal electrodes
Fp1
Fz
F3
F7
T3
C3
Cz
Pz
P3
T5
Fp2
F4
C4

## Slide 60: Temporal lobe epilepsy with the supplementary anterior temporal electrodes

## Slide 61
High-density EEG

## Slide 62
Sphenoidal electrodes

## Slide 63
Intracranial (invasive) EEG

## Slide 64
EEG frequency bands
0,5-4 Hz
4-8 Hz
13-30 Hz
α
δ
ϑ
β
8-13 Hz
1 s
100 uV

## Slide 65: Absence seizure
Notes: Nase práce vychází z klinických pozorování

## Slide 66
Event duration
Period/frequency
Wave duration
Amplitude
Spike-wave complex
Wave
Spike
Spike duration
300 ms
100 uV
Notes: Nase práce vychází z klinických pozorování

## Slide 67: Evoked potentials – recording

## Slide 68
+
Evoked response
Background activity
10x averaging
100x averaging
200x averaging
500x averaging
1000x averaging
3000x averaging
Evoked potentials – averaging

## Slide 69: Brainstem Auditory Evoked Potentials
I - auditory nerve
II - cochlear
III - superior olivary nuclei
IV - lateral lemniscus
V - inferior colliculi
II+III - pons
IV+V - midbrain
Left ear stimulation at 60 dB.

## Slide 70: Visual evoked potentials
Pattern reversal evoked potentials
Or just blinking (infants, comatose patients)

## Slide 71: Visual evoked potentials
Healthy eye
Diseased eye
Demyelination related disease - slower signal propagation

## Slide 72: Consciousness

## Slide 73: Consciousness (awareness)
No universally agreed definition
Basic awareness
  Reacting to environment
  Generating emotions
  Supported by brain stem
Higher forms of awareness
  Awareness of one’s existence
  Cortex required

## Slide 74: Consciousness disorders
Locked-in syndrome
  Patient aware, has sleep-wake cycle
  Quadriplegia and pseudobulbar palsy
  Can communicate using eye and eyelid movements
Minimally conscious state
  Behavioral evidence of self or environmental awareness
    Following simple commands
    Vocalizations or gestures in response to linguistic content or questions
    Attempts to reach objects
    Eye fixation to moving objects
Vegetative state
  No awareness
  Sleep-wake cycle preserved
  No communication, only reflexes (eye opening upon stimulus)
Coma
  No response to even painful stimuli
Brain death

## Slide 75: Glasgow coma scale
Test | Not Testable (NT): Examples | 1 | 2 | 3 | 4 | 5 | 6
Eye (ocular response) | Severe trauma to the eyes | Does not open eyes | Opens eyes in response to pain | Opens eyes in response to voice | Opens eyes spontaneously | N/A | N/A
Verbal (oral response) | Intubation, language disability | Makes no sounds | Incomprehensible sounds | Inappropriate words | Confused and disoriented, but able to answer questions | Oriented to time, person, and place, converses normally | N/A
Motor (motoric response) | Paralysis/hemiparesis | Makes no movements | Abnormal extension | Abnormal flexion | Flexion / Withdrawal from painful stimuli | Moves to localise pain | Obeys commands

## Slide 76: Glasgow coma scale
Should be reported as the sum and individual values, e.g.
  GCS 9 = E2 V4 M3 at 07:35
  GCS 9 = E1c V1t M3 at 07:35 (c … closed, t … tube)
Brain injury classified as
  Minor 15–13
  Moderate 12–9
  Severe 8–3

## Slide 77: Sleep

## Slide 78: What is the sleep?
Basic physiological need
Behavioral state
  Reversible
  Low interaction with environment
  Decrease motor activity
  Stereotype postures

## Slide 79: Polysomnography
Monitoring of various physiological signals during sleep

## Slide 80: Sleep stages
REM (Rapid eye movements)
  Rapid eye movements
  Muscle atonia
    Not in REM behavioral disorder (RBD)
  Increased neuronal activity
  Increased metabolism
  EEG similar to waking
  “Paradoxical sleep”
  Vivid dreams
Non-REM
  Classification NREM 1-3
  Alternatively Stage 1-4
  Low neuronal activity
  The lowest level of the brain metabolism
  Decrease of sympathetic activity
  Muscle tone and reflexes intact

## Slide 81: Sleep EEG
B
A
T
S
Drink
Blood
4-7 Hz
12-30 Hz
8-12 Hz
1-4 Hz
1-4 Hz
12-30 Hz

## Slide 82: Hypnogram, sleep cycles
Cycle duration 90 – 110 minutes
4 – 6 cycles per night

## Slide 83: Physiological changes during sleep

## Slide 84: Physiological changes during sleep
Heart rate
Respiration
Penile erection

## Slide 85: Sleep during development and aging

## Slide 86: Wakefulness
Ascending reticular activating system (ARAS)
  All components innervated by orexin neurons
  Connections to cortex, etc.
Orexin/hypocretin
  Neuropeptide
  Maintains wakefulness
  Only 50 000 to 80 000 orexin neurons in human brain, in lateral hypothalamus
  Lack of orexin neurons -> narcolepsy

## Slide 87: Narcolepsy
Sleep disorder
Low quality of sleep
Initiation with REM sleep
Excessive daytime sleepiness
Sleep attacks during day
Cataplexy
  Sudden atonia while conscious
  Inhibitory descending reticulospinal pathway (like in REM sleep)

## Slide 88: Narcolepsy
Mechanism
  Loss of orexin neurons
Causes
  Genetic predisposition
  Environmental factors
    Autoimmune disorder triggered by H1N1 infection
Treatment
  Amphetamines
  Tricyclic antidepressants
  Orexin
normal hypothalamus
narcolepsy

## Slide 89: Role of sleep
Not entirely elucidated
Important for cognition
  Memory consolidation
Toxin clearing
Immune system more active during sleep
Sleep deprivation
  Followed by sleep compensation
  If severe, can lead to death

## Slide 90: Circadian rhythms

## Slide 91: Circadian rhythm
Changes in behavior due to alternating day and night
Predicting the day and night advantageous
Circadian clock developed in all organisms

## Slide 92: Molecular mechanism
Molecular oscillator in each cell on earth
Principle: The protein product inhibits its own transcription by feedback mechanism
In the human body, the cells need to be synchronized
  Suprachiasmatic nucleus (SCN)

## Slide 93: Synchronization by SCN
Ganglion cells in the retina (not rods or cones)
Send information about daylight to the suprachiasmatic nucleus (SCN)

## Slide 94: Damage to SCN
Normal
SCN lesion

## Slide 95: Free-running period
In constant darkness (or constant light)
The SCN oscillates at approx. 24 hour period
In most humans, around 25 hours

## Slide 96: Chronotherapy
Administration of drugs (or other treatment) at the time when it is most effective/has least adverse effects
  Heart attacks most probable in the morning due to highest blood pressure -> the best time for taking the drugs for blood pressure
  Antiseizure medication administered at the time when most seizure occur
  etc.

## Slide 97: Thank you for your attention
Questions?
Comments?
Suggestions?
kudlaceksystem@gmail.com