## Slide 1: Plasma I ZS 2014 L10 Plasma Diagnostics
Irving Langmuir was born in Brooklyn, New York, on January 31, 1881, as the third of four sons of Charles Langmuir and Sadie, neé Comings. His early education was obtained in various schools and institutes in the USA, and in Paris (1892-1895). He graduated as a metallurgical engineer from the School of Mines at Columbia University in 1903. Postgraduate work in Physical Chemistry under Nernst in Göttingen earned him the degrees of M.A. and Ph.D. in 1906.
The Nobel Prize in Chemistry 1932
Surface Chemistry
Irving Langmuir
Notes: poznamka

## Slide 2: Plasma
Definition of a plasma
Although a plasma is loosely described as an electrically neutral medium of positive and negative particles, a more rigorous definition requires three criteria to be satisfied:
The plasma approximation
Charged particles must be close enough together that each particle influences many nearby charged particles, rather than just the interacting with the closest particle (these collective effects are a distinguishing feature of a plasma). The plasma approximation is valid when the number of electrons within the sphere of influence (called the Debye sphere whose radius is the Debye (screening) length) of a particular particle is large. The average number of particles in the. Debye sphere is given by the plasma parameter Λ.
Bulk interactions
The Debye screening length (defined above) is short compared to the physical size of the plasma. This criterion means that interactions in the bulk of the plasma are more important than those at its edges, where boundary effects may take place
Plasma frequency
The electron plasma frequency (measuring plasma oscillations of the electrons) is large compared to the electron - neutral collision frequency (measuring frequency of collisions between electrons and neutral particles). When this condition is valid, plasmas act to shield charges very rapidly (quasineutrality is another defining property of plasmas)

## Slide 6: Debye shielding 1
A+
e-
The effect of potential – perturbing charge in a plasma are generally much shorter- range than in vacuum because the charges in plasma tend to distribute themselves so as to shield the plasma from the electric field the perturbing charge generates.
The effect can be deduced readily from Poisson’s equation by assuming, for example, that ions do not move but that electrons adopt a thermal equilibrium distribution in which electron distribution is determined by the Boltzmann factor:
n is electron density far from the perturbing charge where potential V is taken as a zero. Poisson’s equation is:
V
ne
ni
ne=ni=n
V=0
If we suppose that eV<<kTe exponential term can be expressed by 1+eV/ kTe
And we obtain:
In Cartesian coordinates,

## Slide 7: Debye shielding 2
V
ne
ni
ne=ni=n
V=0
eV<<kTe,, exponential can be approximated by linear term
lD
In one dimension the solution indicates exponential decrease of potential
 perturbing effect of a charge will tend to penetrate into the plasma only
to the distance of the order of the Debay length lD
lD
In one dimension

## Slide 8: Debye shielding 3
For laboratory plasma with Te=1eV and ne=1011cm-3  lD=20mm
ne=1011cm-3  “distance between particles ~ 2mm; lD=20mm
For afterglow 100K plasma with Te~0.001eV and ne=1010cm-3  lD=2mm
Thus the plasma potential tends to be positive relative to the walls or to any electrically isolated object, such as a large piece of dust or a floating probe.
Plasma in metal cylinder and plasma in glass cylinder…..??!!!

## Slide 9: Debye shielding 4
V
ne
ni
ne=ni=n
V=0
lD
In one dimension the solution indicates exponential decrease of potential
 perturbing effect of a charge will tend to penetrate into the plasma only
to the distance of the order of the Debay length lD
lD
- -
In spherical symmetry Poisson’s equation gives (not in SI!):

## Slide 10: Debye shielding 5
V
ne
ni
ne=ni=n
V=0
lD
lD
- -
N – number of particles in Debye sphere
Rewritten to another form:

## Slide 11: Cylindrical probe
A
Potential
VPl
Vp
Va
Reference electrode
Va

## Slide 12: Langmuir probe Plasma Diagnostics
I.H. Hutchinson
Principle of plasma diagnostics
Cambridge, second edition 2002
Conventional Langmuir probe theory assumes collisionless movement of charge carriers in the space charge sheath around the probe. Further it is assumed that the sheath boundary is well-defined and that beyond this boundary the plasma is completely undisturbed by the presence of the probe. This means that the electric field caused by the difference between the potential of the probe and the plasma potential at the place where the probe is located is limited to the volume inside the probe sheath boundary.
The general theoretical description of a Langmuir probe measurement requires the simultaneous solution of the Poisson equation, the collision-free Boltzmann equation, and the continuity equation with regard to the boundary condition at the probe surface and requiring that, at large distances from the probe, the solution approaches that expected in an undisturbed plasma.
Langmuir Probe in Theory and Practice
by Evgeny V. Shun'ko
Notes: poznamka

## Slide 13: Particle flux
Number of particles of a given species crossing unit area per unit time (from one side) is:
In TD equilibrium
For Ar+ ve/vi > 280
Electric current from the plasma to surface A:
Floating potential – Vf Plasma potential – Vp Probe potential – Vpr
plasma

## Slide 16
Working regimes for Langmuir probe

## Slide 17: Single probe method
Integration over velocity distribution – depends on geometry
In spherical coordinates

## Slide 18: Single probe method
For particles that fall on the probe surface, following equation holds:
Leading to integration limits:

## Slide 19: Single probe method

## Slide 20: Langmuir probe electron current density in retarding region
For Maxwell distribution

## Slide 21: Single probe method
Temperature of the charged particles (usually electrons) is obtained from the first derivative of the probe current:
Number density (of electrons) can be evaluated from the value of probe current at plasma potential:

## Slide 22: Single probe method
Probe is attracting the charged particles

## Slide 23: Single probe method
Probe is attracting the charged particles

## Slide 24: Single probe method
Probe is attracting the charged particles

## Slide 25: Cylindrical probe
Vp=Va - VPl
Vp
Va
-IP
-
Probe characteristic

## Slide 26: Probe circuit

## Slide 27: Floating potential
At floating potential, Vf, Ie=-Ii and we obtain:
For Ar+ plasma me/mi =1/80 000

## Slide 28: Probe characteristic
A
Potential
VPl
Vp
Va
Reference electrode
Va
-IP
Semilogarithmic scale
Linear scale
-
+

## Slide 29: Retarding region for general EEDF
The second derivative necessary for the estimation of the EEDF can be either directly measured (on-line methods) or computed numerically from the experimental data (off-line methods).
Direct calculation

## Slide 30: Retarding region for general EEDF, approximation
Second harmonic method
Digital methods

## Slide 31: Measured EEDF, low temperature afterglow
Linear scale

## Slide 32: Double probe method
The double probe technique is usually applied to measure the electric field in a discharge plasma, but it can also be applied to determine the electron temperature and, at certain experimental conditions, the plasma density.
Denoting the first and second probe by the subscripts 1 and 2, respectively, we can write down the following equations based on Kirchhoff’s laws:
Here U1;2 denotes the probe voltage with respect to the space potential, and Ud is the voltage between the two probes.
The great advantage of this method is its insensitivity to the effect of collisions in the space
charge sheath around the probe.

## Slide 33: RF compensated probe
The center curve is the correct I . V curve. The dashed ones are displaced by ±5V, representing changes in Vs. At the vertical lines, the average Ie between the displaced curves is shown by the dot. The line through the dots is the time-averaged I . V curve that would be observed, differing greatly from the correct curve.

## Slide 34: Probe characteristic measured in oscillating plasma – sinusoidal oscillation of plasma potential
False temperature can be measured
Te*
Te
Te*

## Slide 35: Langmuir probe in plasma containing electronegative gases
+
e-
-
e-
+
-
90% of ions Cl-
100% of ions Ar+
10% of electrons

## Slide 36: Langmuir probe in magnetized plasma

## Slide 37: Current-voltage characteristic in presence of magnetic field

## Slide 38: Langmuir probe setup
ESPion, an Advanced Langmuir
Probe for Plasma Diagnostics

## Slide 39: Rosetta using Langmuir probe
Rosetta using Langmuir probe
The picture below shows Rosetta in space. The large bluish "wings" are the solar panels which provide electricity for all systems onboard the spacecraft. The red circles show the locations of the two sensors of the Langmuir probe instrument, LAP. One of the two sensors is enlarged at the bottom of the picture. The sensor itself is a titanium sphere 50 mm in diameter, looking goldish because of its titanium nitride coating.
ESA's Rosetta mission was launched on 2 March 2004. It has spent ten years in space, passed by two asteroids (2867 Steins in 2008 and 21 Lutetia in 2010) and will reach Comet 67P/Churyumov-Gerasimenko in 2014. Rosetta will follow the comet as it orbits around the Sun, and will be the first mission to attempt a landing onto a comet nucleus.

## Slide 40: Langmuir probe applications
Rosetta using Langmuir probe
Rosetta using Langmuir probe
The picture below shows Rosetta in space. The red circles show the locations of the two sensors of the Langmuir probe instrument, LAP. The sensor itself is a titanium sphere 50 mm in diameter.
Notes: poznamka

## Slide 41: Langmuir probe in magnetic field
The measurement of the plasma potential Φpl by means of the ball-pen probe utilizes the different electron and ion gyroradii in a magnetized plasma.

## Slide 44: Probe circuit
How is the current flowing?

## Slide 45: Langmuir probe setup, reference electrode, closed loop
A
Vp=Va - VPl
Potential
VPl
Vp
Va
Reference electrode
Va
-
+
reference electrode

## Slide 46: EEDF

## Slide 47: Retarding region for general EEDF
The second derivative necessary for the estimation of the EEDF can be either directly measured (on-line methods) or computed numerically from the experimental data (off-line methods).
Direct calculation

## Slide 48: Retarding region for general EEDF, approximation
Second harmonic method
Digital methods

## Slide 49: Langmuir probe -plasma parameters

## Slide 50: Langmuir probe NH4+

## Slide 51: Measured EEDF, high electron temperature

## Slide 52: Measured EEDF, low temperature afterglow
Linear scale

## Slide 53: Current-voltage characteristic in presence of magnetic field

## Slide 54: Variation of the probe characteristics along the flow tube
The decay time is correlated
with the position in the flow tube.
L
Ar+
He+
L

## Slide 55: Evolution of the probe characteristics along the flow tube
Ie2 ~neAPr(Vprobe-Vplasma)
Study of H3+ and H5+recombination

## Slide 56: Langmuir probe FALP - HCOH - formation and recombination

## Slide 57: Langmuir probe setup
Obr 3: Vrchní panel: Průběh elektronové koncentrace po přidáni Ar do rozpadající se plazmy v proudícím He.
Dolní panel: Odpovídající pokles koncentrace metastabilů He(23S).
Vypočtená rychlostní konstanta k = 7×10-11 cm3 s-1, tato hodnota je v dobré shodě s výsledkem Lindingera et al
Obr 4: Vrchní panel: Průběhy potenciálu plazmatu, plovoucího potenciálu a intenzity axiálního elektrického pole. Plné body odpovídají rozpadu v čistém He, který je ovlivňován přítomností metastabilů He(23S).
Otevřené symboly označují data odpovídající směsi He s Ar. V oblasti 0-1 cm probíhá Penningova ionizace.
Dolní panel: Odpovídající průběhy elektronové teploty.

## Slide 58: Langmuir probe - after penning ionization, EEDF
Hem + Ar Ar+ + He + e-

## Slide 59: AISA diagnostics systems
LANGMUIR PROBE

## Slide 60
PULSED STATIONARY AFTERGLOW
20-100ms decay
H3+
e-
a(T)
T
t
dni/dt=-anine
40 cm diameter
UHV - 10-9 Torr
External magnetron
2 Torr of He/Ar/H2
ne(t), ni(t)
AISA
VT - AISA
He/Ar/H2

## Slide 61: Langmuir probe FALP Ar+ dominated plasma

## Slide 62: Probe calibration using recombination of O2+
Langmuir probe measurements
0
10
20
30
40
10
8
10
9
10
10
diffusion
diffusion
He
2
+
O
2
+
He
2
+
Ar
+
O
2
+
n
e
[cm
-3
]
time [ms]
Decays of the electron number density
measured in afterglow with three different dominated ions : He2+, Ar+, O2+
H2O number density, [H2O]  6109cm-3
Influence of impurities

## Slide 63: Langmuir probe Plasma Diagnostics
Notes: poznamka

## Slide 64: EEDF FALP experiment
Notes: poznamka

## Slide 65: EEDF
Notes: poznamka

## Slide 66: Cylindrical probe
A
Vp=Va - VPl
Potential
VPl
Vp
Va
Reference electrode
Va
Detail of ion current
-IP
+IP
-
+
+
Probe characteristic

## Slide 67: Double probe method
The double probe technique is usually applied to measure the electric field in a discharge plasma, but it can also be applied to determine the electron temperature and, at certain experimental conditions, the plasma density.
Denoting the first and second probe by the subscripts 1 and 2, respectively, we can write down the following equations based on Kirchhoff’s laws:
Here U1;2 denotes the probe voltage with respect to the space potential, and Ud is the voltage between the two probes.
The great advantage of this method is its insensitivity to the effect of collisions in the space
charge sheath around the probe.

## Slide 68: RF compensated probe
The center curve is the correct I . V curve. The dashed ones are displaced by ±5V, representing changes in Vs. At the vertical lines, the average Ie between the displaced curves is shown by the dot. The line through the dots is the time-averaged I . V curve that would be observed, differing greatly from the correct curve.

## Slide 69: Probe characteristic measured in oscillating plasma – sinusoidal oscillation of plasma potential
False temperature can be measured
Te*
Te
Te*

## Slide 70: Langmuir probe in plasma containing electronegative gases
+
e-
-
e-
+
-
90% of ions Cl-
100% of ions Ar+
10% of electrons

## Slide 71: THEORIES OF ION COLLECTION
Adjacent to the surface is the Child-Langmuir (CL) sheath, where the electron density ne is negligible. Next is the Debye sheath, in which the electron density ne drops exponentially with V. At the sheath edge x = xs (usually set as the origin), quasineutrality holds, so that ne ≈ni. Here the electron distribution is isotropic (except for the few energetic ones that reach the probe), but the ion distribution is unidirectional, since the probe absorbs all the incoming ions. To reach this state, a presheath region must exist, in which a small electric field accelerates the ions to a velocity cs, giving rise to the Bohm current
Comparison of the slopes of the I2/V curve from various theories
with data from a high-density (n ≈1013 cm-3) helicon plasma

## Slide 72: Reference electrode - Hiden analytical

## Slide 73: Langmuir probe in magnetic field
The measurement of the plasma potential Φpl by means of the ball-pen probe utilizes the different electron and ion gyroradii in a magnetized plasma.