## Slide 1: Plasma light sources
Low Pressure Light Sources, Fluorescent Lamps, Sodium Low Pressure Discharge Lamps, High Pressure Plasma Light Sources, Construction and Operation

## Slide 5
Jean Picard (1620–1682) Astronomer Responsible for the first accurate measurement of the Earth's radius
Jean Picard noticed that the empty space in his mercury barometer glowed as the mercury quivered as he carried the barometer. Francis Hauksbee first demonstrated a gas discharge lamp in 1705. He showed that an evacuated or partially evacuated glass sphere, in which he placed a small amount of mercury, charged with static electricity, could produce light bright enough to read.
Generator built by Francis Hauksbee. From Physico-Mechanical Experiments, 2nd Ed., London 1719

## Slide 6: Geissler tubes
Heinrich Geisler (1814-1879)
Two electrodes in a tube with gas (neon, argon, krypton, xenon, hydrogen, CO2) at low pressure, glow discharge

## Slide 7: Neonové výbojky
Commercially produced by Georges Claude from 1910
0.4 – 3 kPa, glow discharge (mainly positive column)
Orange color (neon)
Other colours using other gases (hydrogen – red, helium – yellow, CO2 – white, mercury – blue)

## Slide 8: Neon glow lamp (doutnavka)
Pressure on the order of hundreds of Pa Two electrodes close to each other, glow discharge (cathode region)
Voltage tester
Circuit breakers, indicators, surge protection, voltage stabilizers, etc.

## Slide 9: CRI – Color Rendering Index
Measure of how natural colors render under an artificial white light source when compared with sunlight
Scale 0 - 100
CRI 95 - 100 → Phenomenal color rendering. Colors appear as they should, subtle tones pop out and are accented, skin tones look beautiful, art comes alive, backsplashes and paint show their true colors.
Used widely in Hollywood production sets, high-end retail stores, printing and paint shops, design hotels, art galleries, and in residential applications where natural colors need to shine brightly.
CRI 90 - 95 → Great color rendering! Almost all colors 'pop' and are easily distinguishable. Noticeably great lighting starts at a CRI of 90. Your newly installed teal-colored backsplash in your kitchen will look beautiful, vibrant, and fully saturated. Visitors begin to compliment the counters, paint, and details of your kitchen, but little do they the lighting is mostly responsible for it looking so amazing.
CRI 80 - 90 → Good color rendering, where most colors are rendered well. Acceptable for most commercial uses. You may not see items as fully saturated as you would like.
CRI Below 80 → Lighting with a CRI below 80 would be considered to have poor color rendering. Under this light, items and colors may look desaturated, drab, and at times unidentifiable (like being unable to see the difference between black and navy-colored socks). It would be difficult to distinguish between similar colors.
https://www.flexfireleds.com/color-rendering-index-cri-and-led-lighting-what-is-cri/

## Slide 10: CRI – Color Rendering Index
Measure of how natural colors render under an artificial white light source when compared with sunlight
Scale 0 - 100
https://www.flexfireleds.com/color-rendering-index-cri-and-led-lighting-what-is-cri/

## Slide 13: Zářivky (Low pressure fluorescent lamp)
Zapojení startéru a tlumivky k zářivkové trubici.
a - vstup, b - tlumivka, c - kompenzační kondenzátor, d - startér, e - bimetalová elektroda, f - odrušovací kondenzátor
A fluorescent lamp tube is filled with a mix of argon, xenon, neon, or krypton, and mercury vapor. The pressure inside the lamp is around 0.3% of atmospheric pressure.
Low pressure arc dicharge

## Slide 14: Zářivky (Low pressure fluorescent lamp)

## Slide 15
CRI – Color Rendering Index, by definition CRI = 100 for incandescent lamp (black body radiation of light bulb)

## Slide 16
Typical fluorescent lamp with rare-earth phosphor | A typical "cool white" fluorescent lamp utilizing two rare-earth-doped phosphors, Tb3+, Ce3+:LaPO4 for green and blue emission and Eu:Y2O3 for red. For an explanation of the origin of the individual peaks click on the image. Several of the spectral peaks are directly generated from the mercury arc. This is likely the most common type of fluorescent lamp in use today.
An older-style halophosphate-phosphor fluorescent lamp | Halophosphate phosphors in these lamps usually consist of trivalent antimony- and divalent manganese-doped calcium halophosphate (Ca5(PO4)3(Cl, F):Sb3+, Mn2+). The color of the light output can be adjusted by altering the ratio of the blue-emitting antimony dopant and orange-emitting manganese dopant. The color rendering ability of these older-style lamps is quite poor. Halophosphate phosphors were invented by A. H. McKeag et al. in 1942.

## Slide 17
Yellow fluorescent lights |  | The spectrum is nearly identical to a normal fluorescent lamp except for a near total lack of light shorter than 500 nanometers. This effect can be achieved through either specialized phosphor use or more commonly by the use of a simple yellow light filter. These lamps are commonly used as lighting for photolithography work in cleanrooms and as "bug repellent" outdoor lighting (the efficacy of which is questionable).

## Slide 18
Spectrum of a "blacklight" lamp |  | There is typically only one phosphor present in a blacklight lamp, usually consisting of europium-doped strontium fluoroborate, which is contained in an envelope of Wood's glass.

## Slide 24: Low Pressure Sodium Lamp
Low-pressure sodium (LPS) lamps have a borosilicate glass gas discharge lamp (arc tube) containing solid sodium and a small amount of neon and argon gas in a Penning mixture (argon-infused neon – has a lower ionization potential, easier to ignite the discharge) to ignite the discharge in the gas. The lamp can be linear (SLI lamp) or U-shaped. When the lamp is first started, it emits a dim red/pink light to heat the metallic sodium; Within a few minutes, as the metallic sodium evaporates, the emission turns to a normal bright yellow. These lamps produce virtually monochromatic light with an average wavelength of 589.3 nm (in fact, the two dominant spectral lines are very close to each other at 589.0 and 589.6 nm). The colors of objects illuminated only by this narrow bandwidth are difficult to distinguish.
High efficiency (up to 206 lm/W) Long lifetime – 18,000 hours, light intensity does not decrease towards the end of service life (consumption increases slightly)
Gradually replaced by other light sources.

## Slide 25
Warm-up phases of a LPS lamp. The faint pink light of the Penning mixture is gradually replaced by the bright monochromatic orange light of the metallic sodium vapor.

## Slide 28
CRI – Color Rendering Index, by definition CRI = 100 for incandescent lamp (black body radiation of light bulb)

## Slide 32: High pressure sodium lamp
An amalgam of metallic sodium and mercury lies at the coolest part of the lamp and provides the sodium and mercury vapor that is needed to draw an arc. The temperature of the amalgam is determined to a great extent by lamp power. The higher the lamp power, the higher will be the amalgam temperature. The higher the temperature of the amalgam, the higher will be the mercury and sodium vapor pressures in the lamp and the higher will be the terminal voltage. As the temperature rises, the constant current and increasing voltage consumes increasing energy until the operating level of power is reached. For a given voltage, there are generally three modes of operation:
The lamp is extinguished and no current flows.
The lamp is operating with liquid amalgam in the tube.
The lamp is operating with all amalgam evaporated.
The first and last states are stable, because the lamp resistance is weakly related to the voltage, but the second state is unstable. Any anomalous increase in current will cause an increase in power, causing an increase in amalgam temperature, which will cause a decrease in resistance, which will cause a further increase in current. This will create a runaway effect, and the lamp will jump to the high-current state (#3). Because actual lamps are not designed to handle this much power, this would result in catastrophic failure. Similarly, an anomalous drop in current will drive the lamp to extinction. It is the second state that is the desired operating state of the lamp, because a slow loss of the amalgam over time from a reservoir will have less effect on the characteristics of the lamp than a fully evaporated amalgam. The result is an average lamp life in excess of 20,000 hours.

## Slide 33: High pressure sodium lamp
In practical use, the lamp is powered by an AC voltage source in series with an inductive "ballast" in order to supply a nearly constant current to the lamp, rather than a constant voltage, thus assuring stable operation. The ballast is usually inductive rather than simply being resistive to minimize energy waste from resistance losses. Because the lamp effectively extinguishes at each zero-current point in the AC cycle, the inductive ballast assists in the reignition by providing a voltage spike at the zero-current point.

## Slide 39: Plasma Displays
Plasma displays were first used in PLATO computer terminals. This PLATO V model illustrates the display's monochromatic orange glow seen in 1981. University of Illinois
In a monochrome plasma panel, the gas is mostly neon, and the color is the characteristic orange of a neon-filled lamp (or sign). Once a glow discharge has been initiated in a cell, it can be maintained by applying a low-level voltage between all the horizontal and vertical electrodes–even after the ionizing voltage is removed. To erase a cell all voltage is removed from a pair of electrodes.

## Slide 40: Plasma displays
Relative spectral power of red, green and blue phosphors of a common plasma display. The units of spectral power are simply raw sensor values (with a linear response at specific wavelengths).

## Slide 41: Plasma displays
Every pixel is made up of three separate subpixel cells, each with different colored phosphors. One subpixel has a red light phosphor, one subpixel has a green light phosphor and one subpixel has a blue light phosphor. These colors blend together to create the overall color of the pixel, the same as a triad of a shadow mask CRT or color LCD. Plasma panels use pulse-width modulation (PWM) to control brightness: by varying the pulses of current flowing through the different cells thousands of times per second, the control system can increase or decrease the intensity of each subpixel color to create billions of different combinations of red, green and blue. In this way, the control system can produce most of the visible colors. Plasma displays use the same phosphors as CRTs, which accounts for the extremely accurate color reproduction when viewing television or computer video images (which use an RGB color system designed for CRT displays).
To produce light, the cells need to be driven at a relatively high voltage (~300 volts) and the pressure of the gases inside the cell needs to be low (~500 torr).